## Slide 1: Speech segmentation: Voiced / Unvoiced / Silence
ECE 6255 — B.H. Juang — Team: Topel, Cruz, Ritz

## Slide 2: Project overview
Goal: label each short-time frame as silence, voiced, or unvoiced.
Why: front-end for recognition, coding, and analysis.
Approach: STE + ZCR + autocorrelation pitch strength; classical DSP only.

## Slide 3: Theoretical foundation
STE E = (1/N) Σ x_w² — high for voiced, very low for silence.
ZCR — high for noise-like unvoiced fricatives; lower for periodic voiced.
R(k) peak in pitch lag range → periodicity → voiced.

## Slide 4: Algorithm pipeline
Frame: ~25 ms, Hamming, ~10 ms hop.
Features per frame → adaptive thresholds → 3-class labels.
Median filter + min run merge → optional boundary heuristics.
Plots + export to results/.

## Slide 5: Implementation (MATLAB)
main.m — entry, file dialog.
compute_features.m — STE, ZCR, pitch strength.
classify_frames.m + smooth_labels.m — decisions + medfilt1.
params.m — all tunables in one place.

## Slide 6: Adaptive thresholds
Silence: STE below a low percentile of the utterance.
Speech mask from STE quantile drives ZCR statistics.
Voiced: high autocorr peak + ZCR below adaptive cutoff.

## Slide 7: Results — plots
Insert figures from results/ after running main.m.
Show example1 (speech) and example2 (synthetic regions).

## Slide 8: Results — metrics
Run evaluate_example2.m.
Report frame accuracy and 3×3 confusion matrix.
Optional: hand labels for more utterances (see evaluation/README.md).

## Slide 9: Code demo
Screen recording: MATLAB → main → pick example_wavs.
Full walkthrough in the 12-minute team video.

## Slide 10: Conclusion & future work
Median smoothing reduces single-frame errors.
Future: spectral flux/centroid, TIMIT comparison, phoneme boundaries.

## Slide 11: References
Rabiner & Schafer, Digital Speech Processing, 2011.
ECE 6255 course materials (Juang).
Code: https://github.com/TopelJL/ECE-6255-Digital-Processing-Speech-Signals-Term-Project